## Slide 1
PHYSICS – Electric circuits

## Slide 2
LEARNING OBJECTIVES
Core •Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays Understand that the current at every point in a series circuit is the same Give the combined resistance of two or more resistors in series State that, for a parallel circuit, the current from the source is larger than the current in each branch State that the combined resistance of two resistors in parallel is less than that of either resistor by itself State the advantages of connecting lamps in parallel in a lighting circuit Describe the action of a variable potential divider (potentiometer) • Describe the action of thermistors and light- dependent resistors and show understanding of their use as input transducers • Describe the action of a relay and show understanding of its use in switching circuits | Supplement Draw and interpret circuit diagrams containing diodes Calculate the combined e.m.f. of several sources in series • Recall and use the fact that the sum of the p.d.s across the components in a series circuit is equal to the total p.d. across the supply • Recall and use the fact that the current from the source is the sum of the currents in the separate branches of a parallel circuit • Calculate the effective resistance of two resistors in parallel Describe the action of a diode and show understanding of its use as a rectifier • Recognise and show understanding of circuits operating as light-sensitive switches and temperature-operated alarms (to include the use of a relay)

## Slide 3
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes

## Slide 4
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes

## Slide 5
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes
Components

## Slide 6
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes
Components
Switch | 
Resistor (fixed) | 

## Slide 7
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes
Components
Switch | 
Resistor (fixed) | 
Resistor (variable) | 
Heater | 

## Slide 8
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes
Components
Cell | 
Battery | 
Resistor (variable) | 
Heater | 

## Slide 9
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes
Components
Cell | 
Battery | 
Thermistor | 
Light dependent resistor (LDR) | 

## Slide 10
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes
Components
Filament lamp | 
Filament lamp | 
Thermistor | 
Light dependent resistor (LDR) | 

## Slide 11
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes
Components
Filament lamp | 
Filament lamp | 
Ammeter | 
Voltmeter | 

## Slide 12
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes
Components
Galvanometer | 
Magnetising coil | 
Ammeter | 
Voltmeter | 

## Slide 13
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes
Components
Galvanometer | 
Magnetising coil | 
Transformer | 
Bell | 

## Slide 14
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes
Components
Fuse | 
Relay (and switch) | 
Transformer | 
Bell | 

## Slide 15
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes
Components
Fuse | 
Relay (and switch) | 
DC Power Supply | 
AC Power Supply | 

## Slide 16
Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays
Draw and interpret circuit diagrams containing diodes
Components
Diode | 
Light emitting diode | 
Diodes only allow current to flow in one direction. They can be used to protect damage to polarised components.

## Slide 19
Series and Parallel Circuits

## Slide 20
Series and Parallel Circuits
Series
Components are in a single loop, and the current flows from one to the next without any branches.

## Slide 21
Series and Parallel Circuits
Series
Components are in a single loop, and the current flows from one to the next without any branches.
If more bulbs are put into the circuit then the bulbs will be dimmer than before.

## Slide 22
Series and Parallel Circuits
Series
Components are in a single loop, and the current flows from one to the next without any branches.
If more bulbs are put into the circuit then the bulbs will be dimmer than before.
If one bulb breaks then the circuit is broken and all components stop working.

## Slide 23
Series and Parallel Circuits
Series
Components are in a single loop, and the current flows from one to the next without any branches.
If more bulbs are put into the circuit then the bulbs will be dimmer than before.
If one bulb breaks then the circuit is broken and all components stop working.
Parallel
Components are connected on different branches of the wire

## Slide 24
Series and Parallel Circuits
Series
Components are in a single loop, and the current flows from one to the next without any branches.
If more bulbs are put into the circuit then the bulbs will be dimmer than before.
If one bulb breaks then the circuit is broken and all components stop working.
Parallel
Components are connected on different branches of the wire.
If more bulbs are added then the lamps stay bright – they take full voltage.

## Slide 25
Series and Parallel Circuits
Series
Components are in a single loop, and the current flows from one to the next without any branches.
If more bulbs are put into the circuit then the bulbs will be dimmer than before.
If one bulb breaks then the circuit is broken and all components stop working.
Parallel
Components are connected on different branches of the wire.
If more bulbs are added then the lamps stay bright – they take full voltage.
If one bulb breaks the components on different branches keep working. Our home circuits are parallel.

## Slide 26
Ammeters can be placed anywhere in a series circuit and will all give the same reading.
http://www.bbc.co.uk/bitesize/ks3/science/energy_electricity_forces/electric_current_voltage/revision/6/
Current in Series and Parallel circuits

## Slide 27
In a parallel circuit the current through each component depends upon its resistance.
Current in Series and Parallel circuits

## Slide 28
In a parallel circuit the current through each component depends upon its resistance.
1.5A
3A
1A
5.5A
The total current flowing around the circuit is equal to the total of all the currents in the separate branches.
Current in Series and Parallel circuits

## Slide 29
In a parallel circuit the current through each component depends upon its resistance.
1.5A
3A
1A
5.5A
The total current flowing around the circuit is equal to the total of all the currents in the separate branches.
A1 = A2 + A3 + A4
Current in Series and Parallel circuits

## Slide 30
In a parallel circuit the current through each component depends upon its resistance.
1.5A
3A
1A
5.5A
The total current flowing around the circuit is equal to the total of all the currents in the separate branches.
A1 = A2 + A3 + A4
5.5 = 1.5 + 3 + 1
Current in Series and Parallel circuits

## Slide 31
Voltage in Series and Parallel circuits
Voltage is measured using a VOLTMETER
To measure the voltage across a component in a circuit the voltmeter must be placed in parallel with it.

## Slide 32
Voltage is measured using a VOLTMETER
In a series circuit the total voltage (PD) of the supply is shared between the various components, so the voltages around a series circuit always add up to equal the source voltage.
Voltage in Series and Parallel circuits

## Slide 33
Voltage is measured using a VOLTMETER
In a series circuit the total voltage (PD) of the supply is shared between the various components, so the voltages around a series circuit always add up to equal the source voltage.
In a parallel circuit all components get the full source voltage, so the voltage is the same across all components
Voltage in Series and Parallel circuits

## Slide 34
Resistance in Series and Parallel circuits

## Slide 35
Resistance in Series and Parallel circuits
In series

## Slide 36
Resistance in Series and Parallel circuits
In series
If resistors are connected in series, the current through each resistor is the same.
I1 = I2 = I3
I1
I3
I2

## Slide 37
Resistance in Series and Parallel circuits
In series
If resistors are connected in series, the current through each resistor is the same.
I1 = I2 = I3
I1
I3
I2
If resistors are connected in series, the potential difference across all resistors is equal to the sum of the potential differences across each resistor.
VT = V1 + V2 + V3
VT
V1
V2
V3

## Slide 38
Resistance in Series and Parallel circuits
In series
If resistors are connected in series, the current through each resistor is the same.
I1 = I2 = I3
I1
I3
I2
If resistors are connected in series, the potential difference across all resistors is equal to the sum of the potential differences across each resistor.
VT = V1 + V2 + V3
VT
V1
V2
V3
The total resistance of a number of resistors in series is equal to the sum of all the individual resistances.
RT = R1 + R2 + R3
R1
R2
R3

## Slide 39
Resistance in Series and Parallel circuits
In parallel

## Slide 40
Resistance in Series and Parallel circuits
In parallel
I1
I2
I3
IT
If resistors are connected in parallel, the total current is equal to the sum of the currents through each resistor.
IT = I1 + I2 + I3

## Slide 41
Resistance in Series and Parallel circuits
In parallel
If resistors are connected in parallel, the total current is equal to the sum of the currents through each resistor.
IT = I1 + I2 + I3
I1
I2
I3
IT
If resistors are connected in parallel, the potential difference across all resistors is the same.
V1 = V2 = V3
V1
V2
V3

## Slide 42
Resistance in Series and Parallel circuits
In parallel
If resistors are connected in parallel, the total current is equal to the sum of the currents through each resistor.
IT = I1 + I2 + I3
I1
I2
I3
IT
If resistors are connected in parallel, the potential difference across all resistors is the same.
V1 = V2 = V3
V1
V2
V3
R1
R2
R3
The total resistance of a number of resistors in parallel is given by the formula:
1/RT = 1/R1 + 1/R2 + 1/R3

## Slide 43
Resistance in Series and Parallel circuits
In parallel
R1
R2
R3
The total resistance of a number of resistors in parallel is given by the formula:
1/RT = 1/R1 + 1/R2 + 1/R3
For example, if:
R1 = 18Ω
R2 = 12Ω
R3 = 6Ω
1/RT = 1/18 + 1/12 + 1/6
= 2/36 + 3/36 + 6/36 = 11/36
RT = 36/11 = 3.27Ω

## Slide 44
LEARNING OBJECTIVES
Core •Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays Understand that the current at every point in a series circuit is the same Give the combined resistance of two or more resistors in series State that, for a parallel circuit, the current from the source is larger than the current in each branch State that the combined resistance of two resistors in parallel is less than that of either resistor by itself State the advantages of connecting lamps in parallel in a lighting circuit Describe the action of a variable potential divider (potentiometer) • Describe the action of thermistors and light- dependent resistors and show understanding of their use as input transducers • Describe the action of a relay and show understanding of its use in switching circuits | Supplement Draw and interpret circuit diagrams containing diodes Calculate the combined e.m.f. of several sources in series • Recall and use the fact that the sum of the p.d.s across the components in a series circuit is equal to the total p.d. across the supply • Recall and use the fact that the current from the source is the sum of the currents in the separate branches of a parallel circuit • Calculate the effective resistance of two resistors in parallel Describe the action of a diode and show understanding of its use as a rectifier • Recognise and show understanding of circuits operating as light-sensitive switches and temperature-operated alarms (to include the use of a relay)

## Slide 46
What is a variable potential divider?

## Slide 47
What is a variable potential divider?
Potential dividers divide up the voltage within a circuit, so that parts of the circuit only receive the voltage they require. They usually consist of two or more resistors in series across a power supply.

## Slide 48
What is a variable potential divider?
Potential dividers divide up the voltage within a circuit, so that parts of the circuit only receive the voltage they require. They usually consist of two or more resistors in series across a power supply.
10Ω
10Ω
6V
3V
In this example, the lower resistor has half the total resistance of the two resistors, so its share of the voltage from the battery is also a half.

## Slide 49
What is a variable potential divider?
10Ω
0-10 kΩ
6V
0-3V
If one of the resistors is replaced by a variable resistor then the output voltage can be varied. In this example, it can range from 0 to 3V, depending upon the setting of the variable resistor.
A circuit such as this one could be used as a radio volume control.

## Slide 50
What is a diode, and how does it rectify?

## Slide 51
What is a diode, and how does it rectify?
A diode is an electrical component that allows current to flow in one direction only. It is polarised with two leads – the anode and the cathode.

## Slide 52
What is a diode, and how does it rectify?
A diode is an electrical component that allows current to flow in one direction only. It is polarised with two leads – the anode and the cathode.
If the anode is connected to a higher voltage than the cathode, then the current will flow from anode to cathode. This is called forward bias.

## Slide 53
What is a diode, and how does it rectify?
A diode is an electrical component that allows current to flow in one direction only. It is polarised with two leads – the anode and the cathode.
If the anode is connected to a higher voltage than the cathode, then the current will flow from anode to cathode. This is called forward bias.
If the diode is reversed, so that the voltage at the cathode is higher than the voltage at the anode, the diode will not conduct electricity. This is called reverse bias.

## Slide 54
What is a diode, and how does it rectify?
Forward bias – the diode has extremely low resistance, so a current flows through it and the bulb lights up.

## Slide 55
What is a diode, and how does it rectify?
Forward bias – the diode has extremely low resistance, so a current flows through it and the bulb lights up.
Reverse bias– the diode has extremely high resistance, so the current does not flow through it and the bulb does not light up.

## Slide 56
What is a diode, and how does it rectify?
Rectification – diodes can be used to convert AC (alternating current) to DC (direct current).
The diode lets the forward part of the AC through, but blocks the backward part.
We can see how the circuit changes the AC input using the trace on a cathode ray oscilloscope (CRO).

## Slide 57
What is a diode, and how does it rectify?
Rectification – diodes can be used to convert AC (alternating current) to DC (direct current).
The diode lets the forward part of the AC through, but blocks the backward part.
We can see how the circuit changes the AC input using the trace on a cathode ray oscilloscope (CRO).

## Slide 58
What is a diode, and how does it rectify?
Rectification – diodes can be used to convert AC (alternating current) to DC (direct current).
The diode lets the forward part of the AC through, but blocks the backward part.
We can see how the circuit changes the AC input using the trace on a cathode ray oscilloscope (CRO).

## Slide 59
What is a diode, and how does it rectify?
Rectification – diodes can be used to convert AC (alternating current) to DC (direct current).
The diode lets the forward part of the AC through, but blocks the backward part.
We can see how the circuit changes the AC input using the trace on a cathode ray oscilloscope (CRO).

## Slide 60
What is a diode, and how does it rectify?
Rectification – diodes can be used to convert AC (alternating current) to DC (direct current).
The diode lets the forward part of the AC through, but blocks the backward part.
We can see how the circuit changes the AC input using the trace on a cathode ray oscilloscope (CRO).
This is called half-wave rectification.

## Slide 61
LEARNING OBJECTIVES
Core •Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays Understand that the current at every point in a series circuit is the same Give the combined resistance of two or more resistors in series State that, for a parallel circuit, the current from the source is larger than the current in each branch State that the combined resistance of two resistors in parallel is less than that of either resistor by itself State the advantages of connecting lamps in parallel in a lighting circuit Describe the action of a variable potential divider (potentiometer) • Describe the action of thermistors and light- dependent resistors and show understanding of their use as input transducers • Describe the action of a relay and show understanding of its use in switching circuits | Supplement Draw and interpret circuit diagrams containing diodes Calculate the combined e.m.f. of several sources in series • Recall and use the fact that the sum of the p.d.s across the components in a series circuit is equal to the total p.d. across the supply • Recall and use the fact that the current from the source is the sum of the currents in the separate branches of a parallel circuit • Calculate the effective resistance of two resistors in parallel Describe the action of a diode and show understanding of its use as a rectifier • Recognise and show understanding of circuits operating as light-sensitive switches and temperature-operated alarms (to include the use of a relay)

## Slide 62
Describe the action of thermistors and light- dependent resistors and show understanding of their use as input transducers

## Slide 63
Describe the action of thermistors and light- dependent resistors and show understanding of their use as input transducers
Thermistor
Light dependent resistor
A transducer is an electronic device that converts energy from one form into another.

## Slide 64
Describe the action of thermistors and light- dependent resistors and show understanding of their use as input transducers
Thermistor
Light dependent resistor
A transducer is an electronic device that converts energy from one form into another.
Thermistor – resistance decreases as the temperature increases.
At low temperatures the resistance of a thermistor is high and little current can flow through them.
At high temperatures the resistance of a thermistor is low and more current can flow through them.

## Slide 65
Describe the action of thermistors and light- dependent resistors and show understanding of their use as input transducers
Thermistor
Light dependent resistor
A transducer is an electronic device that converts energy from one form into another.
Thermistor – resistance decreases as the temperature increases.
At low temperatures the resistance of a thermistor is high and little current can flow through them.
At high temperatures the resistance of a thermistor is low and more current can flow through them.
Thermistor used in a fire-alarm circuit
www.astarmathsandphysics.com
At room temperature, thermistor has a high resistance and voltage to the transistor is too low. As temperature rises, resistance falls, so more current flows to the transistor and the alarm is switched on.

## Slide 66
Describe the action of thermistors and light- dependent resistors and show understanding of their use as input transducers
Thermistor
Light dependent resistor
A transducer is an electronic device that converts energy from one form into another.
Light dependent resistor (LDR) – resistance decreases as the light intensity increases.
In the dark and at low light levels the resistance of an LDR is high, and little current can flow through
In bright light the resistance of an LDR is low, and current can flow through it.

## Slide 67
Describe the action of thermistors and light- dependent resistors and show understanding of their use as input transducers
Thermistor
Light dependent resistor
A transducer is an electronic device that converts energy from one form into another.
Light dependent resistor (LDR) – resistance decreases as the light intensity increases.
In the dark and at low light levels the resistance of an LDR is high, and little current can flow through
In bright light the resistance of an LDR is low, and current can flow through it.
LDR used in a security light circuit
www.buildcircuit.com
In daylight the LDR has a low resistance and a low share of the battery voltage – too low to switch the transistor on. In darkness the LDR resistance increases, so does its share of the battery voltage. This is now sufficient to switch the transistor on, and the bulb lights up

## Slide 68
And finally …..
RELAYS!

## Slide 69
And finally …..
RELAYS!
A relay is a device which uses a low current circuit to switch a high current circuit on or off.

## Slide 70
And finally …..
RELAYS!
A relay is a device which uses a low current circuit to switch a high current circuit on or off.
For example, a very big relay is used in cars for switching the starter motor, because it draws a very big current.

## Slide 71
And finally …..
RELAYS!
A relay is a device which uses a low current circuit to switch a high current circuit on or off.
For example, a very big relay is used in cars for switching the starter motor, because it draws a very big current.
Low current circuit
High current circuit

## Slide 72
And finally …..
RELAYS!
A relay is a device which uses a low current circuit to switch a high current circuit on or off.
For example, a very big relay is used in cars for switching the starter motor, because it draws a very big current.
Low current circuit
High current circuit
When the switch in the low current circuit is closed, it turns the electromagnet on which attracts the iron armature.
1

## Slide 73
And finally …..
RELAYS!
A relay is a device which uses a low current circuit to switch a high current circuit on or off.
For example, a very big relay is used in cars for switching the starter motor, because it draws a very big current.
Low current circuit
High current circuit
When the switch in the low current circuit is closed, it turns the electromagnet on which attracts the iron armature.
The armature pivots and closes the switch contacts in the high current circuit.
1
2

## Slide 74
And finally …..
RELAYS!
A relay is a device which uses a low current circuit to switch a high current circuit on or off.
For example, a very big relay is used in cars for switching the starter motor, because it draws a very big current.
Low current circuit
High current circuit
When the switch in the low current circuit is closed, it turns the electromagnet on which attracts the iron armature.
The armature pivots and closes the switch contacts in the high current circuit.
When the low current switch is opened the electromagnet stops pulling the armature and the high current circuit is broken again.
1
2
3

## Slide 75
LEARNING OBJECTIVES
Core •Draw and interpret circuit diagrams containing sources, switches, resistors (fixed and variable), heaters, thermistors, light-dependent resistors, lamps, ammeters, voltmeters, galvanometers, magnetising coils, transformers, bells, fuses and relays Understand that the current at every point in a series circuit is the same Give the combined resistance of two or more resistors in series State that, for a parallel circuit, the current from the source is larger than the current in each branch State that the combined resistance of two resistors in parallel is less than that of either resistor by itself State the advantages of connecting lamps in parallel in a lighting circuit Describe the action of a variable potential divider (potentiometer) • Describe the action of thermistors and light- dependent resistors and show understanding of their use as input transducers • Describe the action of a relay and show understanding of its use in switching circuits | Supplement Draw and interpret circuit diagrams containing diodes Calculate the combined e.m.f. of several sources in series • Recall and use the fact that the sum of the p.d.s across the components in a series circuit is equal to the total p.d. across the supply • Recall and use the fact that the current from the source is the sum of the currents in the separate branches of a parallel circuit • Calculate the effective resistance of two resistors in parallel Describe the action of a diode and show understanding of its use as a rectifier • Recognise and show understanding of circuits operating as light-sensitive switches and temperature-operated alarms (to include the use of a relay)

## Slide 76
PHYSICS – Electric circuits