## Slide 1
PHYSICS – Electrical quantities (1)

## Slide 2
LEARNING OBJECTIVES
Core •State that there are positive and negative charges • State that unlike charges attract and that like charges repel • Describe simple experiments to show the production and detection of electrostatic charges • State that charging a body involves the addition or removal of electrons Distinguish between electrical conductors and insulators and give typical examples State that current is related to the flow of charge • Use and describe the use of an ammeter, both analogue and digital • State that current in metals is due to a flow of electrons | Supplement State that charge is measured in coulombs • State that the direction of an electric field at a point is the direction of the force on a positive charge at that point • Describe an electric field as a region in which an electric charge experiences a force • Describe simple field patterns, including the field around a point charge, the field around a charged conducting sphere and the field between two parallel plates (not including end effects) • Give an account of charging • Recall and use a simple electron model to distinguish between conductors and insulators Show understanding that a current is a rate of flow of charge and recall and use the equation I = Q / t • Distinguish between the direction of flow of electrons and conventional current

## Slide 3
http://www.physics.upenn.edu/undergraduate/undergraduate-physics-labs/experiments/electric-charge-and-static-electricity
Static Electricity

## Slide 4
http://www.physics.upenn.edu/undergraduate/undergraduate-physics-labs/experiments/electric-charge-and-static-electricity
Static Electricity
Static electricity is all about charges which are not free to move.
As a result they build up in one place, resulting in a spark or shock when they do move.

## Slide 5
http://www.physics.upenn.edu/undergraduate/undergraduate-physics-labs/experiments/electric-charge-and-static-electricity
Static Electricity
Static electricity is all about charges which are not free to move.
As a result they build up in one place, resulting in a spark or shock when they do move.
Insulating materials, such as polythene and perspex, can be charged by rubbing them with a dry woollen cloth.
+
+
+
+
+
+
-
-
-
-
-
-
Perspex
Polythene

## Slide 6
http://www.physics.upenn.edu/undergraduate/undergraduate-physics-labs/experiments/electric-charge-and-static-electricity
Static Electricity
Static electricity is all about charges which are not free to move.
As a result they build up in one place, resulting in a spark or shock when they do move.
Insulating materials, such as polythene and perspex, can be charged by rubbing them with a dry woollen cloth.
+
+
+
+
+
+
-
-
-
-
-
-
+
+
+
+
+
+
-
-
-
-
-
-
Like charges will try to repel each other.

## Slide 7
http://www.physics.upenn.edu/undergraduate/undergraduate-physics-labs/experiments/electric-charge-and-static-electricity
Static Electricity
Static electricity is all about charges which are not free to move.
As a result they build up in one place, resulting in a spark or shock when they do move.
Insulating materials, such as polythene and perspex, can be charged by rubbing them with a dry woollen cloth.
+
+
+
+
+
+
-
-
-
-
-
-
+
+
+
+
+
+
-
-
-
-
-
-
Unlike charges will try to attract each other.

## Slide 8
http://www.physics.upenn.edu/undergraduate/undergraduate-physics-labs/experiments/electric-charge-and-static-electricity
Static Electricity
Static electricity is all about charges which are not free to move.
As a result they build up in one place, resulting in a spark or shock when they do move.
Insulating materials, such as polythene and perspex, can be charged by rubbing them with a dry woollen cloth.
+
+
+
+
+
+
-
-
-
-
-
-
+
+
+
+
+
+
-
-
-
-
-
-
The closer the charges, the greater the force between them.

## Slide 9
Static Electricity
Only electrons move, never the positive charges!

## Slide 10
Static Electricity
Only electrons move, never the positive charges!
+
+
+
+
+
+
Perspex
-
-
-
-
-
-
-
Electrons move from the rod onto the duster.
The rod becomes positively charged, and the duster becomes negatively charged.

## Slide 11
Static Electricity
Only electrons move, never the positive charges!
-
-
-
-
-
-
Polythene
+
+
+
+
+
+
+
Electrons move from the duster onto the rod.
The rod becomes negatively charged, and the duster becomes positively charged.

## Slide 12
Uses of Static Electricity
1. Electrostatic smoke precipitators.
+
+
+
+
+
+
-
-
-
-
-
-
As particles of smoke or dust rise up the chimney they are attracted to the charged plates on either side.

## Slide 13
Uses of Static Electricity
1. Electrostatic smoke precipitators.
+
+
+
+
+
+
-
-
-
-
-
-
As particles of smoke or dust rise up the chimney they are attracted to the charged plates on either side.
2. Spray painting
+
+
+
_
_
_
The spray nozzle is connected to a positive terminal.
Each spray drop is now +ve.
The drops repel and spread out.
The car is connected to the earth (or –ve).
+ve drops attracted to the –ve car.

## Slide 14
Uses of Static Electricity
1. Electrostatic smoke precipitators.
+
+
+
+
+
+
-
-
-
-
-
-
As particles of smoke or dust rise up the chimney they are attracted to the charged plates on either side.
2. Spray painting
+
+
+
_
_
_
The spray nozzle is connected to a positive terminal.
Each spray drop is now +ve.
The drops repel and spread out.
The car is connected to the earth (or –ve).
+ve drops attracted to the –ve car.
3. Photocopiers make use of static to attract black toner to the paper.

## Slide 15
Distinguish between electrical conductors and insulators and give typical examples

## Slide 16
Distinguish between electrical conductors and insulators and give typical examples
CONDUCTORS – allow electrons to pass through them. Metals have ‘free’ electrons between the individual atoms, and this makes them excellent conductors. The free electrons also make them good conductors of thermal energy (heat).
Copper (conductor)

## Slide 17
Distinguish between electrical conductors and insulators and give typical examples
CONDUCTORS – allow electrons to pass through them. Metals have ‘free’ electrons between the individual atoms, and this makes them excellent conductors. The free electrons also make them good conductors of thermal energy (heat).
Copper (conductor)
INSULATORS – electrons are held tightly to their atoms so are not free to move, and so do not conduct electricity (but electrons can be transferred by rubbing – static charging).
PVC
(insulator)

## Slide 18
Distinguish between electrical conductors and insulators and give typical examples
CONDUCTORS – allow electrons to pass through them. Metals have ‘free’ electrons between the individual atoms, and this makes them excellent conductors. The free electrons also make them good conductors of thermal energy (heat).
Copper (conductor)
INSULATORS – electrons are held tightly to their atoms so are not free to move, and so do not conduct electricity (but electrons can be transferred by rubbing – static charging).
PVC
(insulator)
SEMI-CONDUCTORS – neither an insulator or a conductor. Poor conductors when cold, but much better conductors when warm.

## Slide 19
Distinguish between electrical conductors and insulators and give typical examples
CONDUCTORS – allow electrons to pass through them. Metals have ‘free’ electrons between the individual atoms, and this makes them excellent conductors. The free electrons also make them good conductors of thermal energy (heat).
Copper (conductor)
INSULATORS – electrons are held tightly to their atoms so are not free to move, and so do not conduct electricity (but electrons can be transferred by rubbing – static charging).
PVC
(insulator)
SEMI-CONDUCTORS – neither an insulator or a conductor. Poor conductors when cold, but much better conductors when warm.
Eg. Metals (copper, gold) and carbon
Eg. Silicon and germanium
Eg. Plastics, glass, dry air

## Slide 20
So what’s all this ‘current’ stuff about?
State that current is related to the flow of charge.
Use and describe the use of an ammeter, both analogue and digital.
State that current in metals is due to a flow of electrons.

## Slide 21
So what’s all this ‘current’ stuff about?
State that current is related to the flow of charge.
Use and describe the use of an ammeter, both analogue and digital.
State that current in metals is due to a flow of electrons.
Let’s go back to basics and consider what is happening in an electrical circuit.

## Slide 22
So what’s all this ‘current’ stuff about?
State that current is related to the flow of charge.
Use and describe the use of an ammeter, both analogue and digital.
State that current in metals is due to a flow of electrons.
Let’s go back to basics and consider what is happening in an electrical circuit.
Electricity is the flow of electrons around a circuit.

## Slide 23
So what’s all this ‘current’ stuff about?
State that current is related to the flow of charge.
Use and describe the use of an ammeter, both analogue and digital.
State that current in metals is due to a flow of electrons.
Let’s go back to basics and consider what is happening in an electrical circuit.
Electricity is the flow of electrons around a circuit.
Conventional current flow
+
-

## Slide 24
So what’s all this ‘current’ stuff about?
State that current is related to the flow of charge.
Use and describe the use of an ammeter, both analogue and digital.
State that current in metals is due to a flow of electrons.
Let’s go back to basics and consider what is happening in an electrical circuit.
Electricity is the flow of electrons around a circuit.
Electrons actually flow from the –ve to the +ve, opposite to the conventional current flow.
+
-

## Slide 25
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
Electric current will only flow if there are charges which can move freely.

## Slide 26
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
Electric current will only flow if there are charges which can move freely.
Metals have a “sea” of free electrons (-ve charge) that are free to flow through the metal

## Slide 27
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
Electric current will only flow if there are charges which can move freely.
Metals have a “sea” of free electrons (-ve charge) that are free to flow through the metal
This is why metals are such good conductors of electricity.

## Slide 28
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
Electric current will only flow if there are charges which can move freely.
Metals have a “sea” of free electrons (-ve charge) that are free to flow through the metal
This is why metals are such good conductors of electricity.
The flow of charge is called an electric current. The higher the current, the greater the flow of charge.

## Slide 29
State that current is related to the flow of charge.
Use and describe the use of an ammeter, both analogue and digital.
State that current in metals is due to a flow of electrons.
The unit of current is the ampere (A). This is usually abbreviated to the amp.

## Slide 30
State that current is related to the flow of charge.
Use and describe the use of an ammeter, both analogue and digital.
State that current in metals is due to a flow of electrons.
The unit of current is the ampere (A). This is usually abbreviated to the amp.
Current is measured using an ammeter.

## Slide 31
State that current is related to the flow of charge.
Use and describe the use of an ammeter, both analogue and digital.
State that current in metals is due to a flow of electrons.
The unit of current is the ampere (A). This is usually abbreviated to the amp.
Current is measured using an ammeter.
To measure the current flowing through a circuit, the ammeter is connected in series.

## Slide 32
Measuring current
Ammeters can be placed anywhere in a series circuit and will all give the same reading.
http://www.bbc.co.uk/bitesize/ks3/science/energy_electricity_forces/electric_current_voltage/revision/6/

## Slide 33
Measuring current
In a parallel circuit the current through each component depends upon its resistance.

## Slide 34
Measuring current
In a parallel circuit the current through each component depends upon its resistance.
1.5A
3A
1A
5.5A
The total current flowing around the circuit is equal to the total of all the currents in the separate branches.

## Slide 35
Measuring current
In a parallel circuit the current through each component depends upon its resistance.
1.5A
3A
1A
5.5A
The total current flowing around the circuit is equal to the total of all the currents in the separate branches.
A1 = A2 + A3 + A4

## Slide 36
Measuring current
In a parallel circuit the current through each component depends upon its resistance.
1.5A
3A
1A
5.5A
The total current flowing around the circuit is equal to the total of all the currents in the separate branches.
A1 = A2 + A3 + A4
5.5 = 1.5 + 3 + 1

## Slide 37
LEARNING OBJECTIVES
Core •State that there are positive and negative charges • State that unlike charges attract and that like charges repel • Describe simple experiments to show the production and detection of electrostatic charges • State that charging a body involves the addition or removal of electrons Distinguish between electrical conductors and insulators and give typical examples State that current is related to the flow of charge • Use and describe the use of an ammeter, both analogue and digital • State that current in metals is due to a flow of electrons | Supplement State that charge is measured in coulombs • State that the direction of an electric field at a point is the direction of the force on a positive charge at that point • Describe an electric field as a region in which an electric charge experiences a force • Describe simple field patterns, including the field around a point charge, the field around a charged conducting sphere and the field between two parallel plates (not including end effects) • Give an account of charging • Recall and use a simple electron model to distinguish between conductors and insulators Show understanding that a current is a rate of flow of charge and recall and use the equation I = Q / t • Distinguish between the direction of flow of electrons and conventional current

## Slide 38
PHYSICS – Electrical quantities (1)